CIVIL AVIATION AUTHORITY OF NEW ZEALAND APPROVED

# Master Minimum Equipment List

Pacific Aerospace Limited

PAC 750 XL

CAA Type Certificate Number A-14

FAA Type Certificate Number A50CE

EASA Type Certificate Number IM.A.081

Manufacturer: 	PACIFIC AEROSPACE LIMITED

Address: 	R.D.2 HAMILTON AIRPORT

Private Bag 3027

HAMILTON

NEW ZEALAND

Phone:   	(64) 7 843 6144

Fax:       	(64) 7 843 6134

Website:	www.aerospace.co.nz

TABLE OF CONTENTS / LIST OF EFFECTIVE PAGES

Page No:	Subject:	Revision No:	Date:

1	Cover/Title Page 	Original	12 February 2008

2	Table of Contents/ List of Effective Pages	Original	12 February 2008

3	Highlights of Change	Original	12 February 2008

4	Record of Revisions	Original	12 February 2008

5	Definitions 	Original	12 February 2008

6	Definitions 	Original	12 February 2008

7	Definitions 	Original	12 February 2008

8	Preamble 	Original	12 February 2008

9	Preamble 	Original	12 February 2008

10	Preamble 	Original	12 February 2008

11	Guidelines for (O) and (M) Procedures	Original	12 February 2008

21-1	Air Conditioning	Original	12 February 2008

22-1	Autopilot	Original	12 February 2008

23-1	Communications	Original	12 February 2008

25-1	Equipment/Furnishings	Original	12 February 2008

25-2		Original	12 February 2008

26-1	Fire Protection	Original	12 February 2008

27-1	Flight Controls	Original	12 February 2008

28-1	Fuel	Original	12 February 2008

30-1	Ice and Rain Protection	Original	12 February 2008

31-1	Indicating/Recording Systems 	Original	12 February 2008

32-1	Landing Gear 	Original	12 February 2008

33-1	Lights 	Original	12 February 2008

34-1	Navigation 	Original	12 February 2008

34-2		Original	12 February 2008

34-3		Original	12 February 2008

34-4		Original	12 February 2008

35-1	Oxygen 	Original	12 February 2008

RECORD OF REVISIONS

| Revision Number: | Date: | Page Numbers | Initials |
| --- | --- | --- | --- |
| Original Issue | 12.02.08 |  |  |

## HIGHLIGHTS of CHANGE

## DEFINITIONS

- System Definitions.

System numbers are based on the Air Transport Association (ATA) Specification Number 100 and items are numbered sequentially.

  - "Item" (Column 1) means the equipment, system, component, or function listed in the "Item" column.

  - "Number Installed" (Column 2) is the number (quantity) of items normally installed in the aircraft.  This number represents the aircraft configuration considered in developing this MMEL. Should the number be a variable (e.g., passenger cabin items) a number is not required.

  - "Number Required for Dispatch" (Column 3) is the minimum number (quantity) of items required for operation provided the conditions specified in Column 4 are met.

NOTE:  		Where the MMEL shows a variable number required for dispatch, the MEL must reflect the actual number required for dispatch or an alternate means of configuration control approved by the National Airworthiness Authority.

  - "Remarks or Exceptions" (Column 4) in this column includes a statement either prohibiting or permitting operation with a specific number of items inoperative, provisos (conditions and limitations) for such operation, and appropriate notes.

  - A vertical bar (change bar) in the margin indicates a change, addition or deletion in the adjacent text for the current revision of that page only. The change bar is dropped at the next revision of that page.

- "Airplane Flight Manual" (AFM) is the document required for type certification, approved by the New Zealand CAA and referenced on the applicable aircraft airworthiness certificate.

- "As required by CAR" means that the listed item is subject to certain provisions (restrictive or permissive) expressed in the New Zealand Civil Aviation Rules, (CAR’s), or the applicable operating Rules of the State of Registry.

The number of items required by the CAR’s must be operative.

Items installed that are in excess of the CAR’s may be permitted by the operator's MEL to be inoperative if not otherwise required by the MMEL.

When the listed item is not required by CAR’s it may be inoperative for the time specified by repair category.

- "*" symbol in Column 4 indicates the listed item if inoperative, must be placarded to inform and remind the crewmembers and maintenance personnel of the equipment condition.

NOTE:  	To the extent practical, placards should be located adjacent to the control or indicator for the item affected; however, unless otherwise specified, placard wording and location will be determined by the operator.

- "-" symbol in Column 2 and/or Column 3 indicates a variable number (quantity) of the item installed.

NOTE:  	Where the MMEL shows a variable number installed, the MEL must reflect the actual number installed or an alternate means of configuration control approved by the National Airworthiness Authority.

- "Deleted" in the remarks column after a sequence item indicates that the item was previously listed but is now required to be operative if, installed in the aircraft.

- "ER" refers to extended range operations of a two-engine airplane which has a type design approval for ER operations – Not Applicable to this MMEL.

- "Federal Aviation Regulations" (FAR) means the applicable portions of the Federal Aviation Act and Federal Aviation Regulations.

- “Civil Aviation Rules” (CAR) means the applicable portions of the New Zealand Civil Aviation Act and Civil Aviation Rules.

- "Flight Day" means a 24 hour period (from midnight to midnight) either Universal Coordinated Time (UCT) or local time, as established by the operator, during which at least one flight is initiated for the affected aircraft.

- "Icing Conditions" means an atmospheric environment that may cause ice to form on the aircraft or in the engine(s).

- Alphabetical symbol in Column 4 indicates a proviso (condition or limitation) that must be complied with for operation with the listed item inoperative.

- "Inoperative" means a system and/or component malfunction to the extent that it does not accomplish its intended purpose and/or is not consistently functioning normally within its approved operating limit(s) or tolerance(s).

- "Notes:" in Column 4 provides additional information for crewmember or maintenance consideration.  Notes are used to identify applicable material which is intended to assist with compliance, but do not relieve the operator of the responsibility for compliance with all applicable requirements. Notes are not a part of the provisos.

- Inoperative components of an inoperative system: Inoperative items which are components of a system which is inoperative are usually considered components directly associated with and having no other function than to support that system.

(Warning/caution systems associated with the inoperative system must be operative unless relief is specifically authorized per the MMEL).

- "(M)" symbol indicates a requirement for a specific maintenance procedure which must be accomplished prior to operation with the listed item inoperative. Normally these procedures are accomplished by maintenance personnel; however, other personnel may be qualified and authorized to perform certain functions.  Procedures requiring specialized knowledge or skill, or requiring the use of tools or test equipment should be accomplished by maintenance personnel. The satisfactory accomplishment of all maintenance procedures, regardless of who performs them, is the responsibility of the operator. Appropriate procedures are required to be published as part of the operator's manual or MEL.

- "(O)" symbol indicates a requirement for a specific operations procedure which must be accomplished in planning for and/or operating with the listed item inoperative. Normally these procedures are accomplished by the flight crew; however, other personnel may be qualified and authorized to perform certain functions. The satisfactory accomplishment of all procedures, regardless of who performs them, is the responsibility of the operator. Appropriate procedures are required to be published as a part of the operator's manual or MEL.

NOTE:	The (M) and (O) symbols are required in the operator's MEL unless otherwise authorized by the National Airworthiness Authority.

- "Deactivated" and "Secured" means that the specified component must be put into an acceptable condition for safe flight. An acceptable method of securing or deactivating will be established by the operator.

- "Visual Flight Rules" (VFR) is as defined in CAR Part 91. This precludes a pilot from filing an Instrument Flight Rules (IFR) flight plan.

- "Visual Meteorological Conditions" (VMC) means the atmospheric environment is such that would allow a flight to proceed under the visual flight rules applicable to the flight.  This does not preclude operating under Instrument Flight Rules.

- "Visible Moisture" means an atmospheric environment containing water in any form that can be seen in natural or artificial light; For example, clouds, fog, rain, sleet, hail, or snow.

- "Passenger Convenience Items" means those items related to passenger convenience, comfort or entertainment such as, but not limited to, galley equipment, movie equipment, ash trays, stereo equipment, overhead reading lamps, etc.

- Repair Intervals:  All users of an MEL approved under CAR 91, 121, 125, 135 must effect repairs of inoperative systems or components, deferred in accordance with the MEL, at or prior to the repair times established by the following letter designators:

Category A.  Items in this category shall be repaired within the time interval specified in the remarks column of the operator's approved MEL.

Category B.  Items in this category shall be repaired within three (3) consecutive calendar days (72 hours); excluding the day the malfunction was recorded in the aircraft maintenance record/logbook. For example, if it were recorded at 10 a.m. on January 26th, the three day interval would begin at midnight the 26th and end at midnight the 29th.

Category C.  Items in this category shall be repaired within ten (10) consecutive calendar days (240 hours), excluding the day the malfunction was recorded in the aircraft maintenance record/logbook. For example, if it were recorded at 10 a.m. on January 26th, the 10 day interval would begin at midnight the 26th and end at midnight February 5th.

Category D.  Items in this category shall be repaired within 120 consecutive calendar days (2880 hours), excluding the day the malfunction was recorded in the aircraft maintenance record/logbook. For example, if it were recorded at 10 a.m. on January 26th, the 120 day interval would begin at midnight the 26th and end at midnight May 27th.

The letter designators are inserted adjacent to Column 2.

- Engine Indicating Crew Alerting System (EICAS)

Electronic Centralized Aircraft Monitoring System (ECAM)

Electronic Fault Alerting Systems

Or similar systems that provide electronic messages refer to a system capable of providing different priority levels of systems information messages

(e.g., Warning, Caution, Advisory Status and Maintenance).

Any airplane discrepancy message that affects dispatch ability will normally be at status message level (e.g., Advisory Status) or higher.

- "Administrative control item" means an item listed by the operator in the MEL for tracking and informational purposes.

It may be added to an operator's MEL provided no relief is granted, or provided conditions and limitations are contained in an approved document

(I.e. Structural Repair Manual, airworthiness directive, etc.).

If relief other than that granted by an approved document is sought for an administrative control item, a request must be submitted to the National Airworthiness Authority. If the request results in review and approval by the National Airworthiness Authority, the item becomes an MMEL item rather than an administrative control item.

- “***” symbol in Column 1 of the MMEL indicates an item which is not required by regulation but which may have been installed on some models of aircraft covered by the MMEL.

This item may be included on the operator’s MEL after the National Airworthiness Authority has determined that the item has been installed on one or more of the operator’s aircraft.  The symbol, however, shall not be carried forward into the operator’s MEL.

It should be noted that neither this policy nor the use of this symbol provide authority to install or remove an item from an aircraft.

- “Excess Items” means those items that have been installed that are redundant to the requirements of the CAR’s.

- “Day of Discovery” is the calendar day an equipment/instrument malfunction was recorded in the aircraft Technical Log and/or Record. This day is excluded from the calendar days or flight days specified in the MMEL for the repair of an inoperative item of equipment.

This provision is applicable to all MMEL items, i.e., Categories “A, B, C, and D.”

PREAMBLE

The following is applicable for authorized certificate holders operating under Civil Aviation Rules (CAR) Parts 121, 125, and 135: The CAR require that all equipment installed on an aircraft in compliance with the Airworthiness Standards and the Operating Rules must be operative. However, the Rules also permit the publication of a Minimum Equipment List (MEL) where compliance with certain equipment requirements is not necessary in the interests of safety under all operating conditions. Experience has shown that with the various levels of redundancy designed into aircraft, operation of every system or installed component may not be necessary when the remaining operative equipment can provide an acceptable level of safety.

A Master Minimum Equipment List (MMEL) is developed by the original certificating authority, with participation by the aviation industry, to improve aircraft utilization and thereby provide more convenient and economic air transportation for the public.

The approved MMEL includes those items of equipment related to airworthiness and operating regulations and other items of equipment which the type certifying authority finds may be inoperative and yet maintain an acceptable level of safety by appropriate conditions and limitations; It does not contain obviously required items such as wings, flaps, and rudders.

The MMEL is the basis for development of individual operator MELs which take into consideration the operator's particular aircraft equipment configuration and operational conditions. Operator MELs, for administrative control, may include items not contained in the MMEL; however, relief for administrative control items must be approved by the National Airworthiness Authority.

An operator's MEL may differ in format from the MMEL, but cannot be less restrictive than the MMEL.  The individual operator's MEL, when approved and authorized, permits operation of the aircraft with inoperative equipment.

Equipment not required by the operation being conducted and equipment in excess of CAR requirements are included in the MEL with appropriate conditions and limitations.  The MEL must not deviate from the Aircraft Flight Manual Limitations, Emergency Procedures or with Airworthiness Directives.

IT IS IMPORTANT TO REMEMBER THAT ALL EQUIPMENT RELATED TO THE AIRWORTHINESS AND THE OPERATING REGULATIONS OF THE AIRCRAFT NOT LISTED ON THE MMEL MUST BE OPERATIVE.

Suitable conditions and limitations in the form of placards, maintenance procedures, crew operating procedures and other restrictions as necessary are specified in the MEL to ensure that an acceptable level of safety is maintained.

Where an inoperative item is listed in the operators MEL, but the operator considers it necessary to take maintenance action not specified in the MEL, e.g. disconnection of wiring, either an amendment to the MEL must be approved or a design change raised for continued operation in that configuration.

The MEL is intended to permit operation with inoperative items of equipment for a period of time until repairs can be accomplished. It is important that repairs be accomplished at the earliest opportunity. In order to maintain an acceptable level of safety and reliability the MMEL establishes limitations on the duration of and conditions for operation with inoperative equipment.  These must be carried across to an operator MEL unless the operator can provide an equivalent level of safety argument based on statistical data and failure analysis in support of a variation.

The MEL provides for release of the aircraft for flight with inoperative equipment. When an item of equipment is discovered to be inoperative, it is reported by making an entry in the Aircraft Maintenance Record/Logbook as prescribed by CAR. The item is then either repaired or may be deferred per the MEL or other approved means acceptable to the National Airworthiness Authority prior to further operation. MEL conditions and limitations do not relieve the operator from determining that the aircraft is in condition for safe operation with items of equipment inoperative.

When these requirements are met a: Release to Service Certification - in the Aircraft’s Technical Log; or Aircraft Maintenance Record/Logbook entry; or other approved documentation, is issued as prescribed by CAR. Such documentation is required prior to operation with any item of equipment inoperative.

Operators are responsible for exercising the necessary operational control to ensure that an acceptable level of safety is maintained. When operating with multiple inoperative items, the interrelationships between those items and the effect on aircraft operation and crew workload will be considered.

Operators are to establish a controlled and sound repair program including the parts, personnel, facilities, procedures, and schedules to ensure timely repair.

WHEN USING THE MEL, COMPLIANCE WITH THE STATED INTENT OF THE PREAMBLE, DEFINITIONS, AND THE CONDITIONS AND LIMITATIONS SPECIFIED IN THE MEL IS REQUIRED.

# GUIDELINES FOR (O) AND (M) PROCEDURES

The Civil Aviation Authority has identified a need for certain procedures to provide an        adequate level of safety while providing relief for the following items. These procedures must be established by the operator. The following guidelines are to help establish these required procedures:

21-1	(M) 	Maintenance procedure to ensure the drive belt has been removed to prevent interference with other systems.

21-4	(M)	Maintenance procedure to check there is no air leak or mechanical fault which could be a hazard to the aircraft.

22-1	(M)	Maintenance procedure to check that no electrical or mechanical fault exists that will have an adverse effect on any flight control function.

23-4	(O)	Operations procedure to specify how passengers will be briefed.

25-6	(M)	Maintenance procedure to disconnect ELT remote switch from the ELT, secure wires, verify that ELT is operable and that the manual switch is in the arm position.

25-7	(M)	Maintenance procedure to secure Cargo Restraint System so that it cannot be inadvertently utilized.

27-3	(M)	Maintenance procedure to check to ensure that no electrical or mechanical fault exists that will have an adverse effect on any flight control functions.

28-1	(O)	Operations procedure to ensure that the quantity of fuel on board meets the regulatory requirements.

31-2	(O)	Procedure to manually record the takeoff and landing times on the flight record.

Note:	Aircraft Total Time In Service (TTIS) is recorded as the time elapsed between “Wheels OFF” (Take-off), to “Wheels ON” (Landing).

32-1	(O)	Procedure to ensure the aircraft is chocked or pilot remains at controls.

34-9	(O)	Operations procedure to verify status and suitability of navigation fixes prior to flight and to manually tune approach navigation radios.

34-10 	(O)	Operations procedure to establish alternate procedures and to ensure pilot's altitude awareness.

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 21-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 21-0 | AIR CONDITIONING |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 21-1 *** | Air Conditioner | C | 1 | 0 | * | (M) |
| --- | --- | --- | --- | --- | --- | --- |
| 21-2 *** | Fresh Air Vents Cockpit b) Passenger Cabin | C C | 2 - | 0 0 |  | May be inoperative provided: Cockpit ventilation and/or Passenger cabin ventilation at dispatch is acceptable to the flight crew. |
| 21-3 *** | Ventilation Blower System | C | 1 | 0 | * | May be inoperative provided windshield defogging is not required for ground operations. |
| 21-4 *** | Bleed Air Heating System | C | 1 | 0 | * | (M) May be inoperative provided: Windshield defogging is not required; and VFR Flights Only; and Aircraft is not operated into known or forecast icing conditions. |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 22-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 22-0 | AUTO FLIGHT / AUTOPILOT |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 22-1 | Autopilot | C | 1 | 0 | * | (M) May be inoperative for VFR operations. (M) May be inoperative for two-pilot IFR operations. |
| --- | --- | --- | --- | --- | --- | --- |
| 22-2 | Autopilot Disconnect | C | 1 | 0 |  | May be inoperative providing the autopilot is not utilised at less than initial approach altitude. |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 23-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 23-0 | COMMUNICATIONS |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 23-1 | Communication Systems: (VHF, HF, UHF) | C | - | - | * | As required by the operating Rules. |
| --- | --- | --- | --- | --- | --- | --- |
| 23-2 | Cockpit Speaker | C | 1 | 0 |  | May be inoperative provided an operative headset is used by each flight crew. |
| 23-3 *** | Cockpit ICS System | C | 1 | 0 |  | Not required for single pilot operations. |
| 23-4 *** | Passenger Address System 1) Passenger Configuration 2) Cargo Configuration | C C | 1 1 | 0 0 | * | (O) May be inoperative provided a) Alternate normal and emergency procedures and/or operating restrictions are established and utilized, and b) Appropriate oral briefings are given to passengers. |
| 23-5 | Control Yoke Press-to-Talk Switches | C | 2 | 0 |  | May be inoperative provided hand mike on affected side is operative. |
| 23-6 *** | Static Wicks | C | 10 | 5 |  | For VFR flight one may be broken or missing from each control surface. |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 25-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 25-0 | EQUIPMENT / FURNISHINGS |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 25-1 | Passenger Shoulder Harness |  |  |  |  | Included with relief in ATA 25-3. |
| --- | --- | --- | --- | --- | --- | --- |
| 25-2 | Cockpit Shoulder Harness | C | 2 | 1 | * | Right seat shoulder harness may be inoperative for single pilot operations provided seat remains unoccupied. |
| 25-3 | Passenger Seats | C | 8 | 0 | * | All may be inoperative provided: a) Affected seat does not block emergency egress to the aisle or exit; and b) Affected seat is blocked and placarded “DO NOT OCCUPY” Note 1: A seat with an inoperative seatbelt or shoulder harness is considered to be inoperative. Note 2: A seat with an inoperative recline mechanism is considered to be inoperative if the seat back cannot be secured in the up-right position. |
| 25-4 *** | Flotation Equipment | D | - | - |  | Any in excess of those required by the operating Rules may be inoperative. |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 25-2 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 25-0 | EQUIPMENT / FURNISHINGS |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 25-5 *** | Emergency Medical Equipment (Aircraft First Aid Kit) | D | - | - |  | Any in excess of those required by the operating Rules may be inoperative or missing, provided the required distribution is maintained. |
| --- | --- | --- | --- | --- | --- | --- |
| 25-6 | Emergency Locator Transmitter (ELT) 1) Remote Switch | C C | 1 1 | 0 0 | * | As required by the operating Rules. (M) May inoperative provided: a) Remote switch is disconnected from ELT, and b) ELT switch is placed in the ARM position. |
| 25-7 | Cargo Restraint Systems | C | - | - |  | (O) (M) May be inoperative or missing such that the effect is that the item must be considered inoperative, provided the cargo compartment remains empty. |
| 25-8 | Passenger Convenience Item(s) |  | - | 0 |  | Passenger convenience items, expressed in the MMEL, are those related to passenger convenience, comfort or entertainment such as, but not limited to, galley equipment, movie equipment, ashtrays, stereo equipment, overhead reading lamps, etc. Items addressed elsewhere in this document shall not be included. (M) and (O) procedures may be required and included in the air carrier's appropriate document. |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 26-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 26-0 | FIRE PROTECTION |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 26-1 *** | Portable Fire Extinguisher | D | - | - | * | Any in excess of those required by the operating Rules may be inoperative or missing, provided: The inoperative fire extinguisher is tagged inoperative, removed from the installed location and placed out of sight so it can not be mistaken for a functional unit; and Required distribution is maintained. |
| --- | --- | --- | --- | --- | --- | --- |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 10/01/2007 | PAGE: 27-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 27-0 | FLIGHT CONTROLS |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 27-1 | Trim Tab Position Indicators (Rudder, Aileron, Elevator) | C | 3 | 0 | * | May be inoperative provided: a) Tab is visually checked for full range of operation, and b) Tab operation is not affected, and c) Tab is positioned to neutral prior to each departure and neutral position is verified by visual inspection. |
| --- | --- | --- | --- | --- | --- | --- |
| 27-2 | Flap Position Indicator | C | 1 | 0 | * | May be inoperative provided: a) Flaps are visually checked for full travel, and b) Flap operation is not restricted, and c) Flaps are visually checked for proper setting prior to each departure. |
| 27-3 | Electric Elevator Trim | C | 1 | 0 | * | (M) May be inoperative provided manual trim is unaffected. Note: Autopilot, if installed, may be affected. |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 28-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 28-0 | FUEL |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 28-1 | Fuel Quantity Indicators | C | 2 | 1 | * | (O) One may be inoperative provided; a reliable means is used to determine that the fuel quantity on board meets the regulatory requirements for the flight, and The fuel flow and/ fuel pressure indicator are operative. |
| --- | --- | --- | --- | --- | --- | --- |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 30-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 30-0 | ICE AND RAIN PROTECTION |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 30-1 | Pitot Probe and Stall Warning Vane Heater System | B | 1 | 0 | * | May be inoperative for VFR provided the aircraft is not operated in known or forecast icing conditions. |
| --- | --- | --- | --- | --- | --- | --- |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 31-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 31-0 | INDICATING AND RECORDING SYSTEMS |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 31-1 | Clock with sweep second hand or electric digital clock | C | 1 | 0 | * | May be inoperative for VFR; and IFR operations provided the pilot has a watch that indicates in hours, minutes and seconds. |
| --- | --- | --- | --- | --- | --- | --- |
| 31-2 *** | Hour Meter/Flight Hour Recorder | C | 1 | 0 |  | (O) |
| 31-3 *** | Elapsed Timer | C | 1 | 0 |  |  |
| 31-4 *** | Aircraft/Engine Monitoring System | C | 1 | 0 |  |  |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 32-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 32-0 | LANDING GEAR |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 32-1 | Parking Brake | C | 1 | 0 | * | (O) |
| --- | --- | --- | --- | --- | --- | --- |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 33-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 33-0 | LIGHTS |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 33-1 | Cockpit/Flight Compartment and Instrument Lighting System | B | 1 | 0 | * | May be inoperative provided: Sufficient lighting is operative to make each required instrument, control and other device for which it is provided easily readable, and Direct rays and reflections do not impair visibility either inside or outside the aircraft, and Light intensity can be controlled or preset to a satisfactory level for expected conditions, and Lighting configuration at dispatch is acceptable to the flight crew. |
| --- | --- | --- | --- | --- | --- | --- |
| 33-2 | Cabin Lights | C | 1 | 0 | * | May be inoperative provided lighting configuration is acceptable to the flight crew. |
| 33-3 | Anti-Collision Beacon Light System | B | 1 | 0 | * | May be inoperative for day operations. |
| 33-4 *** | Strobe Light System | C | 1 | 0 | * | May be inoperative for day operations. |
| 33-5 | Landing Light – Fixed | C | 1 | 0 | * | May be inoperative for day operations. |
| 33-6 | Position Lights | C | 1 | 0 | * | May be inoperative for day operations. |
| 33-7 | Taxi Light | C | - | 0 | * | May be inoperative for day operations. |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 34-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 34-0 | NAVIGATION |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 34-1 | Altimeter, Adjustable for Barometric Pressure | B | 2 | 1 | * | May be inoperative on Co-pilot’s side for VFR operations only. Note: No relief for single system |
| --- | --- | --- | --- | --- | --- | --- |
| 34-2 | Airspeed Indicator (ASI) | C | 2 | 1 | * | May be inoperative on Co-pilot’s side providing: a) Single pilot operations, and b) No Check and Training operations Note: No relief for single system |
| 34-3 | Gyroscopic Pitch and Bank Indicator Systems (AH) | B | 2 | 1 | * | May be inoperative on Co-pilot’s side for VFR operations only. Note: No relief for single system |
| 34-4 | Gyroscopic Directional Indicator Systems (DG) | B | 2 | 1 | * | May be inoperative on Co-pilot’s side. Note: No relief for single system |
| 34-5 | Gyroscopic Rate of Turn/Slip-Skid Indicators | B | 2 | 0 | * | May be inoperative on: a) The Co-pilot’s side for all flights b) The PIC side for IFR non-passenger carrying operations c) The PIC side for VFR day passenger carrying operations. |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 34-2 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 34-0 | NAVIGATION |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 34-6 | Vertical Speed Indicator | B B | 2 1 | 0 0 | * * | May be inoperative on Co-pilot’s side for all flights. May be inoperative on Pilot’s side except for IFR passenger carrying operations. May be inoperative except for IFR passenger carrying operations. |
| --- | --- | --- | --- | --- | --- | --- |
| 34-7 | ATC Transponders and Automatic Altitude Reporting Systems | C | 1 | 0 | * | May be inoperative provided: a) Enroute operations do not require it’s use, and b) Prior to flight, approval is obtained from ATC facilities having jurisdiction over the planned route of flight. |
| 34-8 *** | Weather Radar/thunderstorm Detection Equipment | C | 1 | 0 | * | As required by the operating Rules |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 34-3 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 34-0 | NAVIGATION |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 34-9 | Navigation Systems (VOR/ILS, Loran, RNAV, MLS, GPS) | C | - | - |  | As required by the operating Rules. |
| --- | --- | --- | --- | --- | --- | --- |
|  | Navigation Databases (GPS) |  |  |  |  | (O) One may be out of currency Both may be out of currency for day VFR. Both may be out of currency for IFR, provided: Current Aeronautical Charts are used to verify Navigation Fixes prior to dispatch; and Procedures are established and used to verify status and suitability of Navigation Facilities used to define route of flight; and Approach Navigation Radios are manually tuned and identified; and ADF or VOR is operational, and route can be flown by ADF or VOR, and No GPS NPA Approaches are conducted in IMC conditions. |
| 34-10 *** | GPWS – Modes 1-5, Test, TAWS | C A | - - | 0 0 | * | May be inoperative for VFR Operations. (O) May be inoperative provided: Alternate procedures are established and used; and Repairs are made within two flight days. |
| 34-11 | DME | C | 1 | 0 | * | May be inoperative provided it is not required as an approach aid. |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 34-4 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 34-0 | NAVIGATION |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 34-12 | ADF | C | 1 | 0 | * | As required by the operating Rules. |
| --- | --- | --- | --- | --- | --- | --- |
| 34-13 | Marker Beacon | C | 1 | 0 |  | May be inoperative provided it is not required as an approach aid. |
| 34-14 *** | Radar Altimeter | C | - | 0 | * |  |
| 34-15 | Altitude Encoder |  |  |  |  | See ATA 34-7 |
| 34-16 | Non-Stabilised Magnetic Compass | B | 1 | 0 | * | May be inoperative provided: a) Any combination of two gyro stabilized compass systems are operative, b) Aircraft is operated with dual independent navigation capability and under positive radar control by ATC on the enroute portion of the flight. OR May be inoperative for flights that are entirely within areas of magnetic unreliability provided at least two stabilized directional gyro systems are installed, operative and Used in conjunction with approved free gyro navigation techniques. Note: No relief for single system |

| NEW ZEALAND CIVIL AVIATION AUTHORITY MASTER MINIMUM EQUIPMENT LIST |
| --- |
| Aircraft Type: Pacific Aerospace Limited 750 XL | REVISION NUMBER: Original DATE: 12/02/2008 | PAGE: 35-1 |

| System & Sequence Numbers | 1. Item | INTERVAL (A=As Specified, B=3 Days, C=10 Days, D=120 Days) |
| --- | --- | --- |
|  |  |  | 2. NUMBER INSTALLED |
| ATA # 35-0 | OXYGEN |  |  | 3. NUMBER REQUIRED FOR DISPATCH |
|  |  |  |  |  | 4. REMARKS OR EXCEPTIONS |

| 35-1 *** | Oxygen System | C | 1 | 0 | * | As required by the operating Rules. |
| --- | --- | --- | --- | --- | --- | --- |